## Slide 1
Image-guided Navigation for Robotics
Hard Constraints Part 2
Rachel Sparks, Ph.D.
Rachel.sparks@kcl.ac.uk
Lecturer in Surgical & Interventional Engineering
School of Biomedical Engineering & Imaging Sciences

## Slide 2: Hard Constraints Week 1 – Recap
    We want to design the following algorithm
        For s(t) ϵ S(t)
        For c ϵ B
        if (!Criteria 1)
        return
        else if (!Criteria 2)
        return
        else if (Criteria 3)
        Sgood(t) ← s(t)
Notes: We have two elements to design – the robot and the images
Hence B is where we should focus our efforts as it is going to give us bigger gains.

## Slide 3: Path Planning Implementation
    We want to design the following algorithm
        For s(t) ϵ S(t)
        For c ϵ B
        if (!Criteria 13)
        return
        else if (Criteria 2)
        Sgood(t) ← s(t)
    Was O now O
    We briefly talked about how to efficiently iterate over imaging data this week we talk about other data representations
Notes: We have two elements to design – the robot and the images
Hence B is where we should focus our efforts as it is going to give us bigger gains.

## Slide 4: Defining Objects
  Up to now we have been using images as look up tables
      Size dependent on number of pixels
      Build up a representation based on little cubes
  Is an image the best representation? We have alternatives
        Surfaces (meshes)
        Points
Notes: Using images as a LUT directly is the simplest approach. However, be aware of the stair casing effect – where your scene representation is essential built up of “cubes” (voxels). This leads to inaccuracies in collision detection that can be on the order of +/- voxel size.

## Slide 5: Image To Surface
  Image rendering (green) and surface (yellow)
  Direct comparison
    Mask has : 14417920 pixels
    Surface has: 99543 polygons
  Often surfaces are going to be more
  computationally efficient?
    Where might this not be the case?
Notes: Answer to Q: It might not be the case for very disperse objects like blood vessels so if you really want to pick the best options check with some use cases!

## Slide 6: Surface Traversal
  Similar to image traversal
    Octree traversal to split triangles based on spatial location
    Same properties as image octree except
        Be aware size of triangle matter – triangles can end up in more than one Octree leaf
        Badly formed triangles can cause problems
        Leaf node need to check triangle collision not box (slightly more complex)

## Slide 7: Surface Traversal
  Similar to image traversal
    Bounding Volume traversal modified to work better with triangles
        Triangles are relatively planar
        Bounding boxes can be oriented to align along major triangle axis
        Leaf node need to check triangle collision – oriented bounding boxes help minimize need for this check (see vtkOBBTree )

## Slide 8: Surface Intersection and Inside Checks
  Both vtkOBBTree and vtkOctreePointLocator have methods to
    check if points are inside/outside of the object
    find the closest polygon in a mesh to a point
    etc.
  There are other types of trees you can try as well!
Notes: Brief note here if you look at the other types of tree I take you to the abstract base class. This is a class you cannot use directly but forces certain behaviours (i.e. FUNCTIONS) for all children classes.
Here we can the abstractcelllocator forces its children to define the idea of intersection, inside, etc. which are all the functions we want to use for our criteria in tutorial. You can always click on the individual children to see how each specific algorithm works and try them out for yourself.

## Slide 9: Image to Points
  Implicit surface
  is some function (typically a polynomial) that takes uses a set of points to define a surface
  For a new point is <0 for points inside the object, >0 for points outside the object.
Example NURBS (Non-uniform rational B-spline)
Bezier Surface – polynomial representation
Notes: Lightweight both in memory (only need to store points) and high in accuracy we can define “implicit” surfaces using sets of points to define an iso surface. The biggest downside is algorithmically this is challenging and can be computationally heavy to define an isosurface if you are using a large set of spline functions
NURBS collision detection: F. Page and F. Guibault, "Collision detection algorithm for NURBS surfaces in interactive applications," CCECE 2003 - Canadian Conference on Electrical and Computer Engineering. Toward a Caring and Humane Technology (Cat. No.03CH37436), Montreal, Quebec, Canada, 2003, pp. 1417-1420 vol.2.
T. Sederberg and R. Farouki, "Approximation by interval Bezier curves" in IEEE Computer Graphics and Applications, vol. 12, no. 05, pp. 87,88,89,90,91,92,93,94,95, 1992.

## Slide 10: Image to Points
  Implicit surface
  is some function (typically a polynomial) that takes uses a set of points to define a surface
  For a new point is <0 for points inside the object, >0 for points outside the object.
  Implementation Details
      Bezier Curve
      Spline
Notes: Lightweight both in memory (only need to store points) and high in accuracy we can define “implicit” surfaces using sets of points to define an iso surface. The biggest downside is algorithmically this is challenging and can be computationally heavy to define an isosurface if you are using a large set of spline functions
NURBS collision detection: F. Page and F. Guibault, "Collision detection algorithm for NURBS surfaces in interactive applications," CCECE 2003 - Canadian Conference on Electrical and Computer Engineering. Toward a Caring and Humane Technology (Cat. No.03CH37436), Montreal, Quebec, Canada, 2003, pp. 1417-1420 vol.2.
T. Sederberg and R. Farouki, "Approximation by interval Bezier curves" in IEEE Computer Graphics and Applications, vol. 12, no. 05, pp. 87,88,89,90,91,92,93,94,95, 1992.

## Slide 11: Image to Points
  Implicit surfaces can be defined using piecewise approximations (De Casteljau's algorithm)
      Recursively split the patch into two segments by finding
          Appropriate Split point
          New control points
        The set of control points can be used to
        define a bounding box for each curve
        As these surfaces are continuous functions
        algorithmically need to define discrete step
        (i.e. precision of system)
Notes: Wolfgang Boehm, Andreas Müller. On de Casteljau's algorithm. Computer Aided Geometric Design 16(7): 587-605, 1999.

## Slide 12: Implicit Surface Traversal
  As in image and surface
      Tree traversal can be used to identify region of curve to consider
      De Casteljau's algorithm can be used to iteratively define a bounding volume split
      For both octree and bounding volume each leaf node must contain enough points to correctly define surface patch in the region covered by the surface node
      Accurate but computational complex
Notes: Klein, J. and Zachmann, G. (2004), Point Cloud Collision Detection. Computer Graphics Forum, 23: 567-576. doi:10.1111/j.1467-8659.2004.00788.x

## Slide 13: Point Cloud Collision Detection
    Define object by a densely populated point cloud (Klein and Zachmann 2004)
      Define a collision as being with a set radius (defined by sampling distance between points)
      Quicker than implicit surfaces
      Much simpler and computationally quick
Notes: Klein, J. and Zachmann, G. (2004), Point Cloud Collision Detection. Computer Graphics Forum, 23: 567-576. doi:10.1111/j.1467-8659.2004.00788.x
Down side is based on your radius you will have some “error” where points very close to the surface i.e. with the radius will not be possible to distinguish from those on the surface.

## Slide 14: Image To Surface
  Image rendering (green) and surface (yellow)
  Direct comparison
  Mask has : 14417920 pixels
  Surface has: 99543 polygons
  Point count: 255787

## Slide 15: Point Cloud Collision Detection
  Define object by a densely populated point cloud (Klein and Zachmann 2004)
      Define a collision as being with a set radius (defined by sampling distance between points)
      Quicker than implicit surfaces
      Much simpler and computationally quick
  As with other object types
    Octrees can be used
    As points have no orientation/volume bounding
    volumes typically not used
    kdTree are tree with a binary partitioning
    of the points sets (similar to bounding volume)
Notes: Klein, J. and Zachmann, G. (2004), Point Cloud Collision Detection. Computer Graphics Forum, 23: 567-576. doi:10.1111/j.1467-8659.2004.00788.x

## Slide 16: Path Planning Implementation
    We want to design the following algorithm
        For s(t) ϵ S(t)
        For c ϵ B
        if (!Criteria 13)
        return
        else if (Criteria 2)
        Sgood(t) ← s(t)
Notes: We have two elements to design – the robot and the images
Hence B is where we should focus our efforts as it is going to give us bigger gains.

## Slide 17: Defining States
  the state of a robot can be represented by a position
        3D surface
        Parametric Line (+thickness)
  Alternatively we can define
      set of controllable tool parameters
      maps tool parameters to tool position
      Linking state to movement parameters allows for
        Robust representation of how the robot moves
        Easier to determine how to control robot
        Can help reduce optimisation space: we need only solve for
Notes: Simple lines and surfaces can help make a problem easy for a path planning perspective but may obscure the relationship between how to control the robot and where the position of the robot should be

## Slide 18: Defining States – Straight Tools
  the state of a robot can be represented by a position
  For a straight tool
      – Starting point
      - Ending point
      Don’t forget some thickness term r
  Note: can drop ; contains information about all time points

## Slide 19: Defining States – Straight Tools
  the state of a robot can be represented by a position
  For a straight tool
      – Starting point
      - Ending point
      Don’t forget some thickness term r
  Note: can drop ; contains information about all time points
    Enumerating all possible states is quick and easy
    Once states enumerated reject based on criteria

## Slide 20: Defining States – Steerable Tools
  the state of a robot can be represented by a position
      At a steady insertion velocity the needle with bend with a radius
      Steering by turning the needle controls the direction of the bend (parameterised by )
  Simplest solution is assume position is a discrete update:
x
y
x
y
v
w
Notes: The state depends on the previous state so discretizing along time can be a useful way to reduce the search space -> basically find viable solutions at increments of t starting early to exclude infeasible trajectories early
Webster, R. J., Kim, J. S., Cowan, N. J., Chirikjian, G. S., & Okamura, A. M. (2006). Nonholonomic Modeling of Needle Steering. The International Journal of Robotics Research, 25(5–6), 509–525. https://doi.org/10.1177/0278364906065388
Patil, S., & Alterovitz, R. (2010). Interactive Motion Planning for Steerable Needles in 3D Environments with Obstacles. Proceedings of the ... IEEE/RAS-EMBS International Conference on Biomedical Robotics and Biomechatronics. IEEE/RAS-EMBS International Conference on Biomedical Robotics and Biomechatronics, 893–899. doi:10.1109/BIOROB.2010.5625965

## Slide 21: Defining States – Steerable Tools
  the state of a robot can be represented by a position
      At a steady insertion velocity the needle with bend with a radius
      Steering by turning the needle controls the direction of the bend (parameterised by )
      More complete solution is given by the instantaneous velocity:
x
y
x
y
v
w
Notes: First three columns take into account material frame rotation and position

## Slide 22: Defining States – Steerable Tools
  the state of a robot can be represented by a position
      At a steady insertion velocity the needle with bend with a radius
      Steering by turning the needle controls the direction of the bend (parameterised by )
  Simplest solution is assume position is a discrete update:
  Due to the iterative nature of the problem
      Best to reject positions at each step of
      Avoid enumerate for solutions that are infeasible early
Notes: The state depends on the previous state so discretizing along time can be a useful way to reduce the search space -> basically find viable solutions at increments of t starting early to exclude infeasible trajectories early
Webster, R. J., Kim, J. S., Cowan, N. J., Chirikjian, G. S., & Okamura, A. M. (2006). Nonholonomic Modeling of Needle Steering. The International Journal of Robotics Research, 25(5–6), 509–525. https://doi.org/10.1177/0278364906065388
Patil, S., & Alterovitz, R. (2010). Interactive Motion Planning for Steerable Needles in 3D Environments with Obstacles. Proceedings of the ... IEEE/RAS-EMBS International Conference on Biomedical Robotics and Biomechatronics. IEEE/RAS-EMBS International Conference on Biomedical Robotics and Biomechatronics, 893–899. doi:10.1109/BIOROB.2010.5625965

## Slide 23: Defining States – Flexible Tools
  the state of a robot can be represented by a position
      Highly dependent on the robot
      Example concentric tube:
Notes: States can vary along the trajectory based on theta and phi!
At least it is a piecewise Bezier function (each segment can be solved independently)

## Slide 24: Defining States – Flexible Tools
  the state of a robot can be represented by a position
  Position dependent on
      Relative length, size, stiffness, and bend of each tube
      Best modelled as a piecewise curvature (actually very similar to Bezier curves)
Notes: States can vary along the trajectory based on theta and phi!
At least it is a piecewise Bezier function (each segment can be solved independently)
C. Bergeles and P. E. Dupont, "Planning stable paths for concentric tube robots," 2013 IEEE/RSJ International Conference on Intelligent Robots and Systems, Tokyo, 2013, pp. 3077-3082.

## Slide 25: Defining States – Flexible Tools
  the state of a robot can be represented by a position
  Position dependent on
      Relative length, size, stiffness, and bend of each tube
      Best modelled as a piecewise curvature (actually very similar to Bezier curves)
  In terms of optimisation this is the worst of all worlds
      Highly complex mathematics to describe relative locations
      Position is not easy to predict from previous state (non-linear relationships between tubes)
      Position is time varying
      Best to use optimisation algorithm to reduce the number of states to consider
          More on how to perform optimisation next week.
Notes: States can vary along the trajectory based on theta and phi!
At least it is a piecewise Bezier function (each segment can be solved independently)
C. Bergeles and P. E. Dupont, "Planning stable paths for concentric tube robots," 2013 IEEE/RSJ International Conference on Intelligent Robots and Systems, Tokyo, 2013, pp. 3077-3082.

## Slide 26: Acceleration Tips and Tricks
  Ensure algorithm and implementation are as optimized as possible before considering these other options.
  They are time consuming to implement. If algorithm and implementation are poor performance gains will be small
      Try to create parallel running threads
      Consider a better programming language
      Take advantage of hardware acceleration

## Slide 27: Parallelisation
  For path planning
      Possible robotic states can be considered as independent
      The problem can be considered embarrassingly parallel
  Subsets of can be identified and run on parallel threads of the same function
      Can maximize computational resources and minimize runtime
      Needs a bit of programming to ensure each call is run on a separate processor core
  Be aware other portions of your algorithm (element iteration, image manipulation) may also be multi-threaded
      In general parallelisation of the lower functions will give you better performance
      Can be useful especially for large computing resources (i.e. many cores)

## Slide 28: Programming Language
  The choice of programming language can have large impacts on runtime
    Lower level languages are usually faster for simple computations
    Learning curve for lower level languages is higher
    Longer development times for lower level languages
Notes: Figure is from () showing run time to compute digits of pi for a large set of programming languages

## Slide 29: Hardware Acceleration
  What hardware you use matters
      CPU computations are slow
      GPU computations are faster
      Embedded/On chip computations are fastest
Notes: Figure is of element wise matrix multiplication