## Slide 1
Image-guided Navigation for Robotics
Image Coordinate Frames
Rachel Sparks, Ph.D.
Rachel.sparks@kcl.ac.uk
Lecturer in Surgical & Interventional Engineering
School of Biomedical Engineering & Imaging Sciences

## Slide 2: Image Coordinate Frames
Every image has its own coordinate frame
Software platforms use this coordinate frame to determine how to render images on screen
Transformations can be applied to alter an image coordinate frame or its rendering
Learning Objectives:
  Understand image coordinates and how 3D Slicer uses this information to render images on screen
  Understand how transformations can be used to alter image coordinates
  Understand how transformations can be used to alter rendering in 3D Slicer

## Slide 3: Image To “World Coordinates”
  Each pixel cind has two additional, implicitly defined properties
    Size/Spacing: real world mm3 of each pixel, [sx sy sz]
    Position/Point: cpnt = (xi,yj,zk)
        Origin: o = (x0, y0, z0)
        Orientation r=
  Can convert pixels between image indices and point coordinates
(0,0,0)
Notes: Specifically for 3D Slicer see the following for a description of the coordinate system: https://www.slicer.org/wiki/Coordinate_systems

## Slide 4: Rendering Pipeline – Overview
  Rendering aims to take N-Dimensional (ND) Data and Display it on a 2D Display screen
    matplotlib.pyplot simply takes the raw pixel data and displays each pixel with a set size
        This does not make use of any of the image specific information (size, origin, orientation)
        Images of different sizes but similar resolutions appear differently
        Images of similar sizes but different resolutions appear the same
Data
2D Screen

## Slide 5: Rendering Pipeline – Overview
  Rendering aims to take N-Dimensional (ND) Data and Display it on a 2D Display screen
    matplotlib.pyplot simply takes the raw pixel data and displays each pixel with a set size
        This does not make use of any of the image specific information (size, origin, orientation)
        Images of different sizes but similar resolutions appear differently
        Images of similar sizes but different resolutions appear the same.
Notes: This is a low-level imaging platform which means you as the developer have to manually specific how items will appear and manually figure out the plane/orientation etc.

## Slide 6: Rendering Pipeline – Slicer Overview
  Rendering aims to take 3-Dimensional (3D) Data and Display it on a 2D Display screen
    In Sicer3D we assume all data is in the same 3D world our “mrmlScene”
    3D world gets projected to different 2D scenes (“Red”, “Yellow”, and “Green” Planes)
Data
3D World
2D Screen
vtkImage
vtkPolyData
mrmlScene
vtkMRML…Node
Red
Yellow
Green
Notes: Data is our vtk objects
The 3D world is a mrmlScene that is a collection of nodes
And our 2D screen is a set of planes – in this example Red, Yellow, and Green corresponding to each of the 2D imaging planes we can select
Overall getting the system to work is a bit more complicated but once done you don’t need to redo for every new dataset!

## Slide 7: vtkMRML*Nodes
  The nodes in 3D Slicer help to define how Data is projected into the 3D World
    We have already seen each node has a name and a unique ID as well as data
  It also stores information to move from
  data to world space
    “TransformNodeID”
  For images we also always need:
    Space
    Origin
    Transformation “IJKToRASDirections”

## Slide 8: vtkMRML*Nodes
  You can move the rendering location of objects using the ‘Transforms’ module
      Note this only changes its appearance on screen not the underlying data!
      We now have two transforms – on describing the underlying data and one describing the transformation applied to the node!
Notes: Example of the brain being shifted up

## Slide 9: vtkMRML*Nodes
  You can move the rendering location of objects using the ‘Transforms’ module
      "Harden" will combine the two transformations into one by altering Origin, Spacing and ITKToRASDirections
Notes: Example of the brain being shifted up

## Slide 10: Different Image Coordinate Frames
Different software implementations implement coordinate frames differently
    Be careful when converting between data types that you understand each coordinate system
    Where possible use in-built tools to perform conversions
    Always sense check coordinates to test your implementation

## Slide 11: Different Image Coordinate Frames
    vtkImage
      When in 3D Slicer vtkImage does not store your origin, spacing, orientation the node does
      Similar to how numpy array of image data does not store origin, spacing orientation
    SimpleITK Image
      Same purpose as a node – this stores origin, spacing, and orientation

## Slide 12: Putting it all together
Images have a size (spacing), origin, and orientation (IJKToRASDirections)
    Not all low lever rendering options (matplotlib) will use all of this information to display images
    Image software that uses all parameters might make different display choices (e.g. what side of the screen is right/left, what axes the 2D imaging planes are shown, etc.)
    Be aware of how coordinate systems might change during data conversions