## Slide 1
Image-guided Navigation for Robotics
Communication Protocols: Pt. 2 Non-API
Rachel Sparks, Ph.D.
Rachel.sparks@kcl.ac.uk
Lecturer in Surgical & Interventional Engineering
School of Biomedical Engineering & Imaging Sciences

## Slide 2: Communication Protocols Part 1 Recap: API
A software intermediary that allows two pieces of software to communicate
Software 2
Variable 1
Variable 2
Software 1
Class 1
Class 2
Process1
Process2

## Slide 3: Communication Protocols Part 1 Recap: API
A software intermediary that allows two pieces of software to communicate
    Comes in many different flavours
    Any command line input, user interface or program you have written or called
USER INTERFACE
FUNCTION
class MyAwesomeClass:
def run(self, var1, var2):
return output
COMMAND

## Slide 4: Communication Protocols Part 1 Recap: Rest API
Client queries a server
Each client message to server contains all necessary information to run algorithm
Each message treated independently

## Slide 5: Publish-Subscribe Pattern
Publisher writes messages
Subscribers read messages
    FIFO (First In – First Out)
Asynchronous – which is great because publisher will continue to write to file even when subscriber is still acting on an earlier message
Lossy format
    No error checking to ensure all messages arrive
    All messages may not be relevant
Very low computational overhead
Allows multiple publishers and subscribers
M1
M2
M3
M4
M5
Publisher
Subscriber
Notes: Asynchronous means write and read may take unequal times.

## Slide 6: Publish-Subscribe Pattern
Topics allow publisher to assign messages by type
Content filters allow subscribers to determine what messages to read
M1
M2
M3
M4
M5
Publisher
Subscriber
Notes: Asynchronous means write and read may take unequal times.

## Slide 7: API Summary
What | Coupling | Scalable | Lossy
Function | Tight | No | No
Signal/Slot | Loose | No | No
REST API | Loose | Yes | Depends
Publish/Subscriber | Loose | Yes | Yes

## Slide 8: API Summary
Covered a lot about how to design (architecture) of communication between applications
Not a lot about how to communicate that information
What | Coupling | Scalable | Lossy
Function | Tight | No | No
Signal/Slot | Loose | No | No
REST API | Loose | Yes | Depends
Publish/Subscriber | Loose | Yes | Yes

## Slide 9: Communication Protocols
Covered a lot about how to design (architecture) of communication between applications
Not a lot about how to communicate that information
What | Coupling | Scalable | Lossy
Function | Tight | No | No
Signal/Slot | Loose | No | No
REST API | Loose | Yes | Depends
Publish/Subscriber | Loose | Yes | Yes
Written in programming language
Compile translates to machine language
Physically manipulate memory on computer

## Slide 10: Communication Protocols
Covered a lot about how to design (architecture) of communication between applications
Not a lot about how to communicate that information
What | Coupling | Scalable | Lossy
Function | Tight | No | No
Signal/Slot | Loose | No | No
REST API | Loose | Yes | Depends
Publish/Subscriber | Loose | Yes | Yes
May not be on the same computer
May not even be on the same operating system
Need another method to transfer information

## Slide 11: Communication Protocols
Covered a lot about how to design (architecture) of communication between applications
Not a lot about how to communicate that information
What | Coupling | Scalable | Lossy
Function | Tight | No | No
Signal/Slot | Loose | No | No
REST API | Loose | Yes | Depends
Publish/Subscriber | Loose | Yes | Yes
May not be on the same computer
May not even be on the same operating system
Need another method to transfer information

## Slide 12: ROS API
ROS combines a REST API (Server-Client) and Publisher-Subscriber
    Ensures loose coupling between modules and highly scalable system
What | Coupling | Scalable | Lossy
Function | Tight | No | No
Signal/Slot | Loose | No | No
REST API | Loose | Yes | Depends
Publish/Subscriber | Loose | Yes | Yes

## Slide 13: ROS2 API
All ROSw programs are built on top of ros_core:
    A build system (colcon)
    Client library interface (rcl)
        How we find services
        Manages names and parameters
        Logging
    ROS middleware interface (rmw)
        Packages to manage specific interfaces with other middleware systems (ros_to_dds)

## Slide 14: ROS2 API
All ROSw programs are built on top of ros_core
Regardless of which packages we are using messages (.msg) are generated and passed between processes to control behavior
Enables flexibility in terms of which packages and processes are running.
Messages supported in python, c and c++
as well as vendor specific APIs

## Slide 15: ROS2 Build Tools
ROS is organized into workspaces that define a set of packages to be loaded and cross referenced with each other.
    At any one time the base ROS2 workspace and one additional workspace may be loaded
    The additional workspace is overlaid
    Each package is identified by a unique name; overlaid workspaces are preferred when duplicates exist
    In your workspace you can create as many packages as you like switching between workspaces enables rapid testing of different implementations.
Note Colcon has replaced ament and catkin but you will still see references to these other build tools as well

## Slide 16: ROS2 Build Tools
How to create a workspace can be found here.
How to create a package can be found here.
These are the two fundamental steps to master to begin programming in ROS2.

## Slide 17: ROS2 Message Handling
Message passing in ROS2 has two fundamental types
  Publisher/subscriber:
    Publishers send messages out at a fix rate on a topic.
    Subscribers receive any message on the topic with the correct type.
    This enables a many-to-many lossy coupling
    Publishers and subscribers can be started in any order
  Service/client
    Clients send a request for data
    Services process the request and send back a response
    This enables a one-to-one lossless coupling
    Services must be started before the client to appropriately receive the data
In the upcoming weeks we will talk more about message implementation

## Slide 18: ROS2 Messages
Need to use the API to determine exact format
    Bool, char, string, int, float, double, etc
    Combined into some simple combo
    Each value has a corresponding unique field name to identify it uniquely
    Specification can be found in a .msg file
msg.linear.x=4*double(rand())/double(RAND_MAX)-2
msg.angular.z=6*double(rand())/double(RAND_MAX)-3
pub.publish(msg)

## Slide 19: Communication Protocols
Covered a lot about how to design (architecture) of communication between applications
Not a lot about how to communicate that information
What | Coupling | Scalable | Lossy
Function | Tight | No | No
Signal/Slot | Loose | No | No
REST API | Loose | Yes | Depends
Publish/Subscriber | Loose | Yes | Yes
Data transfer lossyness depends on communication protocol
Server-client information in robots should be lossless for safety reasons

## Slide 20: Transmission Control Protocol (TCP)
TCP guarantees a lossless transmission of all necessary data
Ensures security and correctness of transfer
    Server recognizes the client as being a valid client
    Server can receive the message from the client
    Client recognizes the server
    Client can receive the messages from the server
To reduce potential of losing the entire message it is broken up into packets
    After packet transmission missing packets are tested for
    Server will query client to resend missing packets

## Slide 21: Transmission Control Protocol (TCP) – 3 way handshake
A handshake is used to establish a reliable communication port between client and server
    The open channel will remain open for the entirety of the transmission
    SYN: query server and provide sequence number (so server knows what packets to send where)
    SYN/ACK: Server acknowledges receipt of message and relays its sequence number (so client know what packets to listen to)
    ACK: Client acknowledges receipt of message

## Slide 22: Transmission Control Protocol (TCP) – Data Packet
Once channel is open all data packets are transmitted along it
Checksum allows us to verify all data is present in packet
Acknowledgement messages passed back to client
    Client should track packets without acknowledgements
    Those without acknowledgement get resent
Timeouts and loss packets can result in an
inability to receive messages on low quality
networks
Increases lag time as entire message must
be transmitter prior to server processing

## Slide 23: ROS2 TCP/IP
Implicitly when we start ROS2 we have an IP address
    ROS_DOMAIN_ID defines this (read here for advice on setting this)
    This parameter can allow you to pass messages between computers and/or robots. Nodes with different will ROS_DOMAIN_ID not send and receive messages
Can also send and receive information over a TCP with the right software.
    In imaging/medicine OpenIGTLink is this system
    ROS2 has an external package ROS2_IGTLink_Bridge supporting this
    Network parameters (port, IP address) are treated as package parameters assigned to a node when created.
Notes: Youtube video explaining this here: https://www.youtube.com/watch?v=qSjNQC2AT_4

## Slide 24: Summary
In this lecture we talked about lossy data transfer methods including:
    REST API
    Publisher/Subscriber
ROs2 uses these data transfer methods and:
    We discussed the inbuilt tools for these in ROS2
    Where in ROS2 to find message and TCP specific parameters and nodes
    Highlighted some useful packages for transfer information