## Slide 1
Image-guide Navigation for Robotics
Feedback Control
Rachel Sparks, Ph.D.
Rachel.sparks@kcl.ac.uk
Lecturer in Surgical & Interventional Engineering
School of Biomedical Engineering & Imaging Sciences

## Slide 2: Robot Control Diagram
Plan
What is our goal?
What action should the robot take to reach goal
Sense
Where is the robot in the world?
What is the state of the robot?
Act
Alter state of the robot
Robot
*
*Can be achieved through external sensors

## Slide 3: Robot Control Diagram
Plan
What is our goal?
What action should the robot take to reach goal
Sense
Where is the robot in the world?
What is the state of the robot?
Act
Alter state of the robot
Motor Controller
Path Planning
Distance sensors
Cameras
Position sensors
Robot

## Slide 4: What is a Robot?
Plan
What is our goal?
What action should the robot take to reach goal
Sense
Where is the robot in the world?
What is the state of the robot?
Robot
Act
Alter state of the robot
Revise Plan
Update the plan

## Slide 5: What is a Robot?
Plan
What is our goal?
Path Planning
Sense
Distance sensors
Cameras
Position sensors
Robot
Act
Motor Controller
Revise Plan
Feedback Control

## Slide 6: Feedback Control
  The aim of feedback control is to ensure the goal state is reached with
      Minimal delay
      Minimum steady state error
      As quickly as possible
      Stability – i.e. will converge to a final solution

## Slide 7: Feedback Control
  Unlike in ROS2 where we can set a joint to a given state:
      Motors apply force to move a joint – friction, damping, or external forces can all cause a joint motion to deviate from the desired state
      Over time small errors tend to be multiplicative and cause drift that may need to be corrected
      The state of the world can be dynamic – i.e. the world may change relative position or another state in response to the movement in the robot that may require updating the plan.

## Slide 8: Feedback Block Diagram
Controller
System
Sensor
Reference
(i.e. Plan)
Measured Output
Measured Error
System Input
System Output
Feedback Controller
+
-

## Slide 9: Feedback Block Diagram
Controller
System
Sensor
Reference
(i.e. Plan)
Measured Output
Measured Error
System Input
System Output
Feedback Controller
+
-
C(s)
F(s)

## Slide 10: Feedback Design
    The goal is to pick an appropriate feedback function F(s) to appropriately alter the forward function C(s) and converge to a reference state R (i.e. minimize measurement error)
    The entire system has a closed loop transfer function (Laplacian Space)
Reference
(i.e. Plan)
Measured Error
System Output
+
-
F(s)
C(s)
Feedback
Signal
x(t)
y(t)
R
e(t)

## Slide 11: Feedback Algorithm Design
  Care must be taken to ensure H(s) is stable
        Bounded input-bounded output (BIBO): for any input x(t) < B the output will also be y(t) < B
        The poles of H(s) must have real negative values (Laplacian Transform/Bode Plot)

## Slide 12: Follower Robot
  The goal is to keep R1 at a fixed distance from R2.
    R2 moves at a constant speed
    Input[]: On-Off DC motor
    Output []:distance between R1 and R2

## Slide 13: Follower Robot – Feed forward Only

## Slide 14: Proportional Control
    Linear feedback control proportional to the measured error e(t)
      where is the gain, is the control output and is the control output when the reference R have been achieved
    Advantage: easy to control and tune – small will ensure error remains bounded
    Disadvantages:
        Slow to converge – as you near the goal the change in state gets smaller and smaller
        Must carefully select to reduce overshooting and ensure convergence

## Slide 15: Follower Robot – Proportional Control

## Slide 16: Follower Robot – Proportional Control

## Slide 17: Follower Robot – Proportional Control

## Slide 18: Follower Robot – Proportional Control

## Slide 19: Integral Control
    Feedback control proportional to the integral of the measured error.
      where is the gain.
    Over time the feedback will grow
    Advantage: Large steps after sufficient time has passed,
    Disadvantage: Unstable over long time scales. as
Notes: In practive integral control only is not an appropriate feedback controller but….

## Slide 20: Proportional Integral Control
    Initially proportional control dominates, overtime integral control will dominate
    Advantages: converges to the desired solution
    Disadvantages: slow to converge, still prone to overshooting

## Slide 21: Follower Robot – PI Control

## Slide 22: Follower Robot – PI Control

## Slide 23: Derivative Control
  Responds to the change in error over time
  Advantage: have a rapid response to changes in the system
  Disadvantages: sensitive to noise in sensors, unstable
Notes: Also in practice combined with Proportional controller

## Slide 24: PID Controller
  Combines proportional, integral, and derivative control and has the best system response
  Advantages: rapid convergence, can be precisely tuned to precisely fit to a given problem
  Disadvantages: tuning the parameters between the three components can be difficult
Notes: K_i in both integral and derivative controls are not

## Slide 25: Follower Robot – PID Control

## Slide 26: Transfer Functions
Feedback System | Transfer Function
P | 
PI | 
PD | 
PID | 
Feedback System | Transfer Function
P | 
PI | 
PD | 
PID | 

## Slide 27: Feedback Control Summary
  Feedback control is needed in real world systems to
      Remedy systemic issues — friction, manufacturer variability in parts,
      Account for sensor error – noise in measurements, drift in localization
      Correct for variability – applied effort for motors, external forces, change in object positions
  Feedback requires considering
      What information (P,I,D) to consider for error measurements
      What is the desired time response (fast or slow?, robust to noise?)
      Stability of the Transfer function – really require full course on Control Theory.