## Slide 1
Image-Guided Navigation for Robotics
Feedback Control in ROS2
Rachel Sparks, Ph.D.
Rachel.sparks@kcl.ac.uk
Lecturer in Surgical & Interventional Engineering
School of Biomedical Engineering & Imaging Sciences

## Slide 2: ROS Robot Controllers
Currently in ROS we are assuming
    Perfect control over individual joints – we can specify an angle of a joint precisely
    Perfect knowledge on the state of the robot – we know the precise configuration of all joints
This allows us to focus on the path planning and trajectory implementation without considering
    How to translate desired state to robot position
    Noisy measurements
    Incomplete measurements
    Feedback control
In this lecture we are going to focus on how to alter elements of our simulation to take these factors into account

## Slide 3: Joint State Controller
Publishes the specific configuration of all joints in a robot
    The joint may have some hard limits in terms of the range of positions it is allowed to take
    Hard collisions between other objects can be taken into account (as in MoveIt!)
    Can also link joints by creating dependent_joints using the mimic tag
<joint name="arm1_to_arm2"
type="continuous">
<origin rpy="0 0 0" xyz="0 0 10"/>
<axis xyz="0 1 0" />
<parent link ="arm1"/>
<child link="arm2"/>
<limit effort="30" velocity="1.0"
lower="-0.75" upper = "0.75"/>
</joint>
<link name="arm2">
<visual>
<geometry>
<cylinder length="5" radius="0.75"/>
</geometry>
<origin rpy="0 0 0" xyz="0 0 2.5"/>
</visual>
<collision>
<geometry>
<cylinder length="5" radius="1"/>
</geometry>
</collision>
</link>

## Slide 4: Proper Joint Controllers
Rather than setting fixed position as in joint_state_controllers the more realistic option are:
    JointEffortController: control the effort on a specific joint to update position
    JointVelocityController : control the effort on a specific joint to update position
Other physical properties of your robot such as mass (), inertia, damping, friction, and stiffness will affect the behavior of joints for these controllers.

## Slide 5: Adding Physical Constraints – Link information
Update the physical properties of a link to account for
    Mass (kg)
    Moment of Inertia (must be symmetric)
    Note these cannot apply to your base link
These are only taken into account for effort controllers
<link name="arm2">
<visual>
<geometry>
<cylinder length="5"
radius="0.75"/>
</geometry>
<origin rpy="0 0 0" xyz="0 0 2.5"/>
</visual>
<collision>
<geometry>
<cylinder length="5" radius="1"/>
</geometry>
</collision>
<inertial>
<mass value="10"/>
<inertia ixx="0.4" ixy="0.0" ixz="0.0"
iyy="0.4" iyz="0.0" izz="0.2"/>
</inertial>
</link>

## Slide 6: Adding Physical Constraints – Joint information
Update the physical properties of a joint to account for
    Damping (Newton*meter)
    Friction (Newton*meter/second)
These are taken into account for velocity and effort controllers
<joint name="arm1_to_arm2" type="continuous">
<origin rpy="1.57 1.57 0" xyz="0 0 10"/>
<axis xyz="0 1 0" />
<parent link ="arm1"/>
<child link="arm2"/>
<dynamics damping="1" friction="2"/>
</joint>

## Slide 7: Adding Physical Constraints – Limits
Set hard limits that enforce maxima (and minimum for position)
  Velocity ( <velocity)
  Effort (<effort)
  Position ( >lower, <upper)
<joint name="arm1_to_arm2" type="continuous">
<origin rpy="1.57 1.57 0" xyz="0 0 10"/>
<axis xyz="0 1 0" />
<parent link ="arm1"/>
<child link="arm2"/>
<dynamics damping="1" friction="2"/>
<limit effort="30" velocity="1.0"
lower="-0.75" upper = "0.75"/>
</joint>

## Slide 8: Adding Physical Constraints – Soft Limits
Set hard limits that enforce maxima (and minimum for position)
  Velocity ( <velocity)
  Effort (<effort)
  Position ( >lower, <upper)
Soft limits: limits that can be overcome by “more force”
  < sort_upper_limit+
  k_position*velocity

## Slide 9: Adding Physical Constraints – Soft Limits
Set hard limits that enforce maxima (and minimum for position)
  Velocity ( <velocity)
  Effort (<effort)
  Position ( >lower, <upper)
Soft limits: limits that can be overcome by “more force”
  < sort_upper_limit+
  k_position*velocity
  Soft limits must be less than hard limits
<joint name="arm1_to_arm2" type="continuous">
<origin rpy="1.57 1.57 0" xyz="0 0 10"/>
<axis xyz="0 1 0" />
<parent link ="arm1"/>
<child link="arm2"/>
<dynamics damping="1" friction="2"/>
<limit effort="30" velocity="1.0"
lower="-0.75" upper = "0.75"/>
<safety_controller
soft_lower_limit ="-0.5"
soft_upper_limit ="0.5"
k_position="1" k_velocity="1"/>
</joint>

## Slide 10: Conversion between controllers
ros2_control collection of general controllers
  can be used to instantiate position, velocity, and effort controllers.
  contains forward and differential drive controllers
  Implements PID and other feedback controllers
Use a publisher to monitor position, velocity, and effort concurrently for a given joint or robot
    For that specific joint it should be easy to monitor how these three parameters interact
    You can only go “up” the tree :i.e effort->velocity->position not position ->velocity->effort
effort_controllers/joint_position_controller: is given a joint_position computes the effort necessary to achieve that position.
effort_controllers/joint_velocity_controller: is given a joint_velocity computes the effort necessary to achieve that position.

## Slide 11: TurtleSim Example – Proportional Control
while self.euclidean_distance(goal_pose) > distance_tolerance:
# Linear velocity in the x-axis.
vel_msg.linear.x = K_d * self.linear_diff(goal_pose)
# Angular velocity in the z-axis.
vel_msg.angular.z = K_d * self.angular_diff(goal_pose)
# Publishing our vel_msg
self.velocity_publisher.publish(vel_msg)
# Publish at the desired rate.
self.rate.sleep()
# Stopping our robot after the movement is over.
vel_msg.linear.x = 0
vel_msg.angular.z = 0
self.velocity_publisher.publish(vel_msg)
Git example: https://gitlab.com/rsparks/7mri0070/-/tree/master/ROSWeek8Lecture

## Slide 12: TurtleSim Example – Proportional Control

## Slide 13: TurtleSim Example – Proportional Control
= 5 goal pose = (6, 7)

## Slide 14: TurtleSim Example – Proportional Control 2
= 5 goal pose = (9, 1)

## Slide 15: Feedback Control
PID controller package: provides general purpose and generalized PID controller
  Define which joints are involved dof_names
  Define the reference_and_state_interfaces (“position” and/or “velocity”)
  Define command_interface (“position” or “velocity”)

## Slide 16: Feedback Control
PID controller package: provides general purpose and generalized PID controller
  Define which joints are involved dof_names
  Define the reference_and_state_interfaces (“position” and/or “velocity”)
  Define command_interface (“position” or “velocity”)

## Slide 17: Plotting Feedback Control
Controller introspection publishes controller values to the topic~/introspection_data/full
Rqt_plot can be used to plot data
rqt_plot ~/introspection_data/full

## Slide 18: ROS – General Feedback Control
Ros_control is the general purpose controller framework
Integrates controllers, joint states and joint commands (limits & effort transmissions)

## Slide 19: ROS – General Feedback Control
MoveIt 2 and specifically MoveItControllerManager
    Takes as input a list of controllers for a robot
    Passes controller properties to MoveIt 2
    Turns controllers on/off as the kinematics solution solve indicates

## Slide 20: MoveIt2 Planning Package
In this and next week tutorial we will be using MoveIt2 for motion planning of our robots
This is a powerful tool that
    Using KDLKinematicsPlugin to perform robotic kinematics (only for serial robots!) or IKFast for inverse kinematics
    Open Motion Planning Library which are a collection of sampling-based motion planning algorithms
    All wrapped into a Robot Commander so at a high level you can move the robot to a specific pose, along a given path (given as way points), or perform a specific action.
Note this makes use of several other libraries and packages in ROS2 – as with most open-source code use what is already available to save your time.
Notes: Kinematics: https://ros-planning.github.io/moveit_tutorials/doc/kinematics_configuration/kinematics_configuration_tutorial.html?highlight=kdl
IKFast: https://ros-planning.github.io/moveit_tutorials/doc/ikfast/ikfast_tutorial.html
OMPL: https://ros-planning.github.io/moveit_tutorials/doc/ompl_interface/ompl_interface_tutorial.html#ompl-settings